## Slide 1: Seizure presentation

## Slide 2: Outline
What do they look like?
Timeline - Review recent/extreme examples
Framework for theories
Go through theories – which clues are in favor/opposed?
Timeline of events
Timeline of a mouses pipeline life cycle
Possible directions
Go through every possibility and weigh any evidence

## Slide 3: What do they look like

## Slide 4: What do they look like - Variable

## Slide 5: What do they look like – restricted to certain depths
This is our primary indicator that this is biological and not motion artifact or electrical artifact
(Motion artifact could also induce a rebound of the baseline spike rate)

## Slide 6: What do they look like - Repetitive
But this must not always be true given that some events occur on different subsets of probes

## Slide 7: What do they look like - Phy
Difference between NS and RS?

## Slide 8: What do they look like - LFP
Witnessed online 3x for one mouse (confirmed post hoc) – Large event, High frequency relative to normal LFP,
followed by saturation as best I can recall (likely display not amplifiers)
Then very quiet
Before returning to baseline (id the area I was watching was not normally completely quiet)
"large event followed by flatish LFPs" - Dan D

## Slide 9: Wen have they happened?

## Slide 10: What do they look like - Followup characterization
Percentage of units involved
Split by RS/NS/Opto-tagged
Split by depth (putative Ctx/Hippocampus/Deep)
Look at waveforms during the event and recovery
LFP – classification may be easier, size estimate may be more accurate, are there any that don't show in the spiking?

## Slide 11: Framework for theories
1. Something is causing the mice to develop epilepsy before they reach us
2. Insertion of the probes causes leads to seizures
3. Something electrical causes the seizures during the experiment
Threshold Theory – 1+2/1+environmental change
1+3
2+3?
1 masquerading as a 2 or 3 (happens during habs in 325 or surgery/recovery)
With each of these possibilities I think it will be helpful to think about how to differentiate them from each other?
  Which mice would we expect the seizures to occur in?
  Would we expect to detect all of them or could they be happening and be undetected?
  Would they always happen in the same place?
  Would we expect them to vary in size?
  Would we expect to see multiple? Or just one?
  Would we expect to see them evenly throughout the session? Or in a stress/task/insertion dependent distribution?
  Difference between Day1 and Day2?

## Slide 12: Theory 1: Developing epilepsy
How can we distinguish this from the other two?
  Look for seizures in mice that do not undergo the full neuropixels experiment
  Try to find a causative factor that has changed

## Slide 13: Theory 1: Developing epilepsy
  Visual coding (~200)
  Corbett and Sam's Pilot (17)
  Design and Build phase (~8?)
  Any mice that received surgery prior to March 2020 (15)
  Caveat: Confound of water restriction and age (S&C, D&B and pre-covid mice were 200+)

## Slide 14: Theory 1: Developing epilepsy
Supporting evidence:
  No evidence of seizures in past pipeline animals
  Visual coding (~200)
  Corbett and Sam's Pilot (17)
  Design and Build phase (~8?)
  Any mice that received surgery prior to March 2020 (15)
  Caveat: Confound of water restriction and age (S&C, D&B and pre-covid mice were 200+)

## Slide 15: Theory 1: Developing epilepsy
Supporting evidence: Increased Seizure rate outside of experiments

## Slide 16: Theory 1: Developing epilepsy
Supporting evidence: Increased Seizure rate outside of experiments

## Slide 17: Theory 1: Developing epilepsy
Supporting evidence: Increased Seizure rate outside of experiments
Limitations:
  Seems to lag behind – we would actually expect it to preceed our rates
  Aren't sure if this is a detection bias
  Haven't seen anything unusual in Ophys/Leslie/Ethan/Ultra mice as far as we know

## Slide 18: Theory 1: Developing epilepsy
Supporting evidence: Seizure rate across lines
Seems to be worst in SSTs and best in C57s
  We would expect any health related issue to affect trangenics more
Caveat: It is difficult to interpret differences in line because of their uneven distribution in time

## Slide 19: Theory 1: Developing epilepsy
Supporting Evidence: Age at Surgery

## Slide 20: Theory 1: Developing epilepsy
Supporting:
  lack in VC mice,
  Lack in previous behavior mice
  Presence during behavior training – seems to be increasing
  rate in C57s vs VIPs vs SSTs
  age at surgery
Maybe against:
  Variability in location
  Never happens on both experiment days
  time during the session (settle data?)
Against:
  lack in eslie, ethan, ultra mice
  rate in ohpys mice?
  Bias day1 > day2

## Slide 21: Theory 1: Developing epilepsy
What can we look for?
  Check more thuroughly in ophys mice
  Continue shallow insertions
  Look for changes at different points in the pipeline
  More factor analysis

## Slide 22: Theory 2: Probe insertion
How can we distinguish this from the other 2?
Bleeding
  seizure rate should correlate with evidence of bleeding
  mainly on our rig, with no increase outside the experiment, or drastically more common on our rig
Damage to a specific area
  Only during experiment
  Should see this in OPT

## Slide 23: Theory 2: Probe insertion
Supporting Evidence:
  Correlation with deep damage/bleeding

## Slide 24: Theory 2: Probe insertion
Supporting Evidence:
  Time during session

## Slide 25: Theory 2: Probe insertion
Supporting Evidence:
  Bias Day1 > Day2

## Slide 26: Theory 2: Probe insertion
Supporting evidence: Variability in location
  Mainly Supports bleeding, not specific structure

## Slide 27: Theory 2: Probe insertion
Supporting Evidence:
  Bias Day1 < Day2

## Slide 28: Theory 2: Probe insertion
Maybe Supporting Evidence:
  Anatomical anomalies
  Always on window side
Thalamic ‘blob’ 10/12 with seizures
Enlarged Hippocampus 4/4 with seizures

## Slide 29: Theory 2: Probe insertion
Supporting Evidence:
  Correlation with deep bleeding
  Time during the session
  Bias day1 < day2
  Variability in location
  Present (N =2) in a nick steinmetz Visual Cortex insertion
  Dan denman saw them – associated them with Stress
Maybe Supporting:
  Anatomy - thalamus blob, enlarged hippocampus, divots
  Never happens on both days
Against:
  didn't see it in the past. Something must have changed and we can't figure out what.

## Slide 30: Theory 2: Probe insertion
What can we look for?
  Changes in the probes (sharp/unsharp, New/Old)
  Changes/variation in probe insertion depth, location or angle
    RL location
    Probe F shimming
  Look in opt for what structures the probes pass through – any that we rarly hit before?

## Slide 31: Theory 3: something electrical
This ones the most far fetched, but is motivated by some things we don't fully inderstand
  .5V difference between OPT box/wall ground and mouse. Another PI who observd seizures thought this was problematic
  Depth death occurs after some time and appears to be contagious – requires headstage replacement
  We never figured out what was causeint the amplifier "blackout" in VC when we were in extreference – could be that there is some buildup that needs to dissapate, and it does so in a different way in tip reference
  Might be dependant on where the tips are?
  What was causing the lick artifact and why does a nonconductive surface solve it?
How can we distinguish this from the other 2?
  Only on the rig (similar to 2)
  Except would not necessarily correlate with bleeding
  I would expect theat we ALWAYS detect these. Although this is not guaranteed I suppose.

## Slide 32: Threshold theory
Supporting evidence:
  Hematoma

## Slide 33: Theory 3: something Electrical
Contrary evidence:
  Distribution of non-seizure intervals

## Slide 34: Theory 2: Something Electrical
Supporting Evidence:
  Most others who have seen them have been multi-probe neuropixels users
Maybe against:
  Most of the supporting evidence for the previous theories
  Never happens on both days
  time during the session
Against electrical:
  Distribution over time
  Bias day1/day2
  Variability in location
  Distrubution of inter-seizure intervals

## Slide 35: Theory 3: something electrical
What can we look for?
  Changes in the rig
    Probes
    Headstages
    Lickspout
    Grounding wires

## Slide 36: Other options
1 masquerading as a 2 or 3
  We cause epilepsy after handoff, but its not due to beleding, damage or electrical
  Ammonia, surgical window implantation, temperature, change in dehydration, stress of experiment
  Look for:
    Changes in these procedures

## Slide 37: Biggest Clues:
Other Evidence:
Two severely dehydrated mice had seizures – Really bad ones too I believe?
Connection with Dura/bleeding during window removal?

## Slide 38: Timeline of events
Our seisures, Wellness report seizures
Humidifier, High ammonia, airflow change, reduced bedding, cage change rate reduced
Down HVAC system
Cage changes
Sharpened probes, new probes, new headstages, NP3 cartridge
RL targeting, probe F Angle
Lickspout changes
Hematoma, divots
cutains jan 2020
any hvac issues (could affect air out through the ducts - are these disconected? 2/16 - 4/9 or 4/24 when replaced, unclear if there were undetected issues before this.
removal of NP2, so one of them isn't direct anymore, , - 1/15 2021
addiitons of synologies (adds heat source to room?)
addition of face cam -NP1 as soon as we got back in june, it had face cam, NP0 - june 30th started using and it had face cam
Started kwik-casting the agarose holes
Switched all mice to 3ul
lickspouts accurate? New lickspouts? MPE solonoid calibration
Brief ACSF filter change
New agarose mixtures
Changed image set (we have 1 seizure in an H mouse though)
Dipping probes in water
Careful adjustment of bumping
Sev gone (keeping mouse in room)

## Slide 39: Timeline of a mouses life
Birth
Genotyping (tail snip)
Weaning
Group housing?
Surgery (P45-60?)
Recovery
ISI
Baseline weight established
Water restriction
Behavior training
Habituation
Insertino window implantation
Experiments

## Slide 40: Interventions
What have we tried to rule out
heating pad/water bath temp
ACSF, agarose powder
lickspout material – may merit more analysis?
sharpened/unsharpened
6 new probes - but then agarose calibrated?
Groudning to PXI box
extra settle time
working on:
depth of insertion?
ammonia and being kept out of cage
plastic window adhesive
Cleaning the rigs better
What else could we try?
6 new headstages/probes
Probe F in a differnet place
Non-water restricted mice

## Slide 41: Possible directions that require more work than inclusion of an additional factor
Can we identify them in habs/ophys?
  Pupil size? Running/behavior anomalies (machine learned?)
Deep dive into the most serious ones, or the C57s
Start using severity instead of seizure/no seizure
  Hard to quantify severity rigorously right now
Online or immediate seizure analysis – slice promptly after?
  Could sor the settle data while the experiment is occuring. I'm going to try this this week
  Anything else we could do if we ID seizure psitive? Wait longer? Try to deliver water in distributed chunks to see if that is connected
Measure potential between OPT and mouse on NP4
Probe F location on OPT and surface
Behavior – slight decrease in performance? Seems like we should assess this before data release
LFP – What do these look like? can we determine size of area affected? Can we detect seizures that did not affect the unit activity?

## Slide 42: Factors with negative results so far
surgeon
Surgery damage
Genotype (ish?)
Baseline weight
daily water normalized by basline weight
Ages/time between pipeline steps *(other than age at surgery)
Number of habs (after handoff)
Compression
Opt damage

## Slide 43: Negative Results

## Slide 44: Negative Results

## Slide 45: Negative Results

## Slide 46: Negative Results

## Slide 47: rate in C57s vs VIPs vs SSTs
What does this tell us?
  Could give insight into whether some of the fluctuations are from changes in the rate of trangenics or real underlying changes over time
  Tells us whether SSTs really Are worse and C57s really are better

## Slide 48: No seizures: visual coding
Seems to indicate that 6 probes alone are not sufficient
  Water restriction may be a significant change

## Slide 49: No seizures: Previous behavior animals
Seems to indicate that 6 probes alone, and water restriction and behavior are not alone sufficient for seizures

## Slide 50: No Seizures: Leslie and ethan mice
something in the colony (like an infection) is not alone sufficent
  (different surgeon, prep, insertion location, stim etc)

## Slide 51: Rate in ophys mice/our mice during training
Seems to indicate that something is happening before the mice get to us that makes them predisposed to seizures

## Slide 52: Observation N=1 from nick stienmetze
Seems to indicate that the location of insertion (visual cortex) matters
Was this mouse water restricted? Sharpened probe? How deep?
Observed in any other mice? Has he checked?

## Slide 53: Time during session
Seems to be biased towards the beginning of the session
Suggests that it is related to something that happens at the beginning or changes throughout the session
insertio

## Slide 54: Thalamus blobs/swollen hippocampus
7/9 had seizures
Alsways on the insertion side
  This implies it is either due to the window implantation
    In which case we should see it in ophys mice/sahars mice
  Or due to the probe insertion
    In which case we should not see them in shallow insertions

## Slide 55: Hydroencephalopothy? Enlarged ventricles?
X/X had seizures
Tends to be on opposite side? I think we saw this in VC sometimes too – might be due to window implant/headpost?